6. ENGINEERING SYSTEMS REQUIREMENTS

B20 EXTERIOR ENCLOSURE

********************************************************************************************************** 
SYSTEMS REQUIREMENTS
EXTERIOR ENCLOSURE TEMPLATE  09/22

Instructions for using this template: There are template files for each UNIFORMAT Level 2 Group Elements. This template is for Group Element B20-EXTERIOR ENCLOSURE. Text such as this is hidden text that will not print when the hidden text box in "Print/Options" is un-checked.

The Architectural Team Member must edit this template for the requirements of the project. The SYSTEMS REQUIREMENTS are intended to define items that are required throughout the facility or on a system wide basis that is common to several rooms. Room-specific requirements are defined in the Part 3 Chapter 5 ROOM REQUIREMENTS section. Coordinate with the lead programmer for ROOM REQUIREMENTS. Editing is required where brackets [ ] appear. Delete all building elements that are not required for the project. If additional elements or sub-elements are required for the project that do not appear in the template, refer to the NIST UNIFORMAT II publication for additional building element numbers and descriptions. The Uniformat II Work Breakdown Structure can be found at www.wbdg.org/ndbm/ . Coordinate with the PERFORMANCE TECHNICAL SPECIFICATION SECTION B20 to ensure that performance requirements are provided for all of the Building Elements listed here and that paragraph numbering matches.

Provide for systems to be utilized by coordination with Part 3, Chapter 4.3 Exterior Character in allowance for the desired requirements for exterior appearance.
**********************************************************************************************************

********************************************************************************************************** 
NOTE: Consider each exterior enclosure component relative to Part 2 UFGS Section 01 33 29, Sustainability Requirements and Reportingand UFC 1-200-02, High Performance and Sustainable Building Requirements.
**********************************************************************************************************

SYSTEM DESCRIPTION
This system consists of the exterior shell of the facility, which includes all vertical and horizontal exterior closure such as exterior walls, exterior windows, and exterior doors. This system excludes roofing (See System B30, Roofing).  Include load bearing exterior walls here, and not in System B10, Superstructure.  Structural frame elements at exterior such as columns, beams, and spandrels are included in Superstructure, with only the applied exterior finishes (e.g., paint, stucco) being included here.  Finishes to the inside face of walls which are not an integral part of the wall construction will be included in System C30, Interior finishes.

GENERAL SYSTEMS REQUIREMENTS
   B2010 EXTERIOR WALLS

[Provide a ventilated, rain-screen, exterior wall system composed of the Exterior Closure and the Exterior Wall Backup Construction indicated below.]

[Provide cavity wall exterior wall systems composed of the Exterior Closure and Exterior Wall Backup Construction indicated below.]

********************************************************************************************************** 
NOTE: Barrier wall systems indicated below should only be used for storage, warehouse, and other types of facilities where moisture intrusion is acceptable.  Use one of the two above systems for all critical facilities. 
**********************************************************************************************************

[Provide a single thickness, barrier wall composed of the Exterior Closure construction indicated below.]

B201003 INSULATION & VAPOR RETARDER

Provide continuous insulation, vapor retarder, water-resistive barrier, and air barrier to meet or exceed requirements of project's energy savings requirements as indicated by applicable     American Society of Heating, Refrigerating, and Air-Conditioning Engineers (ASHRAE) 90.1 calculations called for in     Unified Facilities Criteria (UFC) 1-200-02, High Performance and Sustainable Building Requirements, and meeting minimum building envelope insulation requirements of UFC 3-101-01, Architecture.

Provide a continuous air barrier to control air leakage into, and out of conditioned spaces. The air barrier must encompass all elements of the facility that are exposed to the outside environment or outside environmental conditions such as roof, walls, floors, and compartmentalized unconditioned portions of the facility such as garages, and negatively pressurized spaces.  Permanently seal penetrations through the air barrier, joints in the air barrier, adjoining construction, and transitions to different air barrier materials.

********************************************************************************************************** 
NOTE: Barrier materials can provide an air barrier function, a moisture barrier/ vapor retarder function, a water resistive barrier function, or any combination of the three functions.  Barrier materials can serve more than one function therefore the air barrier may be combined with a moisture barrier or water resistive barrier, if the barrier material chosen can provide multiple functions.  A moisture barrier and the water resistive barrier can only be effective in a prescribed locations, the air barrier can be located anywhere in the wall assembly.

NOTE: Include the bracketed sentence below if the facility meets the requirements stated in UFC 3-101-01, Architecture and the air barrier is to be field tested in accordance with RFP Part 4, B20).
**********************************************************************************************************

[Confirm air barrier compliance with Air Barrier Performance Test in RFP Part 4 B20, Exterior Enclosure.]

********************************************************************************************************** 
NOTE: Building envelope thermal imaging is a step towards achieving designed potential energy savings and comfort. Include the bracketed sentence below if thermal imaging of building envelope is required. Coordinate with air barrier performance testing and construction schedule, as thermal imaging after interior finishes are being applied is not conducive to remedies.
**********************************************************************************************************

[Provide thermal envelope performance testing through infrared thermography in accordance with RFP Part 4. Coordinate thermal imaging testing with air barrier testing construction schedule.]

Provide a continuous water resistive barrier in accordance with UFC 3-101-01, Architecture. The water resistive barrier must resist liquid (bulk) water from being absorbed into the back-up wall assembly if water leaks, penetrates, or seeps past the exterior enclosure cladding system.

Provide a vapor pressure analysis and hygrothermal analysis in accordance with UFC 3-101-01, Architecture. Determine if a moisture barrier/ vapor retarder is required and where it would be located.  Include analysis and conclusion in the design analysis for the project, refer to Part 2 Section 01 33 10.05 20, Design Submittal Procedures. If required by the analysis, provide a moisture barrier/ vapor retarder to restrict the flow of moisture through the exterior enclosure.

Include written and graphic descriptions of exterior enclosure barrier materials and location within the wall as a part of the Contractor provided design analysis.  Identify in the analysis the continuous boundary limits of the air barrier and of the zone or zones to be field tested for building air tightness.

Provide contract drawings that indicate each exterior enclosure barrier location and the materials that make up the barriers. Detail the following barrier conditions;

1.	Typical conditions at wall sections.

2.	Barrier treatment at wall openings.

3.	Intersections with other exterior enclosure assemblies and materials. Include intersections at roof and floors.

4.	Intersections with counter flashing.

5.	Inside and outside corners.

6.	Preservation of air and water tightness at anchors for materials that cover the barrier.

7.	Treatment to seal barrier penetrations such as conduits, pipes, electric boxes, and fixtures.

8.	Indicate air barrier perimeter, if facility is segmented into areas that are not within the air barrier envelope.

B201005 EXTERIOR LOUVERS & SCREENS

Provide exterior louvers and screens as shown on definitive drawings.

********************************************************************************************************** 
NOTE:  Use the following where the building will be subject to hurricane force winds, or where extra storm protection would be desirable.
**********************************************************************************************************

B201009 EXTERIOR PAINTING AND COATINGS

Provide field applied exterior coatings for all items that are not prefinished, and to prefinished items when required to provide a color other than a standard prefinished color.

B201010 EXTERIOR JOINT SEALANTS

Provide exterior application of joint sealants to seal joints and prepare for finish material installation.

B2030 EXTERIOR DOORS

B203006 BLAST RESISTANT DOORS

Provide special doors used for blast resistance as shown on definitive drawings. Doors shall be custom fabricated steel doors to receive a painted finish. All frames shall be non-corroding galvanized steel.

B203008 EXTERIOR DOOR HARDWARE

Provide locking device or integrnal locking devices as shown on definitive drawings.  The locking device is government furnished and contractor installed item.

--End of Section--