6. ENGINEERING SYSTEMS REQUIREMENTS

B30 ROOFING

********************************************************************************************************** 
SYSTEMS REQUIREMENTS
ROOFING TEMPLATE 06/23

Instructions for using this template: There are template files for each UNIFORMAT Level 2 Group Elements. This template is for Group Element D30-ROOFING. Text such as this is hidden text that will not print when the hidden text box in "Print/Options" is unchecked.

The Architectural Team Member must edit this template for the requirements of the project. The SYSTEMS REQUIREMENTS are intended to define items that are required throughout the facility or on a system wide basis that is common to several rooms. Room-specific requirements are defined in the Part 3 Chapter 5 ROOM REQUIREMENTS section. Coordinate with the lead programmer for ROOM REQUIREMENTS. Editing is required where brackets [ ] appear. Delete all building elements that are not required for the project. If additional elements or sub-elements are required for the project that do not appear in the template, refer to the NIST UNIFORMAT II publication for additional building element numbers and descriptions. The Uniformat II Work Breakdown Structure can be found at www.wbdg.org/ndbm/

Coordinate with the PERFORMANCE TECHNICAL SPECIFICATION SECTION B30 to ensure that performance requirements are provided for all of the Building Elements listed here and that paragraph numbering matches.
**********************************************************************************************************

********************************************************************************************************** 
NOTE: Consider each roofing component relative to UFC 3-110-03, Roofing, Part 2 UFGS Section 01 33 29, Sustainability Requirements and Reportingand UFC 1-200-02, High Performance and Sustainable Building Requirements.
**********************************************************************************************************

B30 GENERAL SYSTEM DESCRIPTION

Provide watertight roof systems compatible with the facility function, construction, and service conditions.  Provide complete roof system design and construction services for the entire new facility roof system, including all ancillary and incidental work necessary for a complete, new, watertight roof system installation.

Submittal Requirements: Components of a minimum roof submittal include the roof plan, method of drainage, standard details and details unique to the project, wind load calculations and requirements.

Provide a Pre-Design Roofing Conference (if required in RFP Part 4) and Pre-Roofing Conference to assure roof design and construction is properly coordinated before construction begins.

********************************************************************************************************** 
NOTE:  The minimum roof live load will be not less than 20 psf (960 Pa).  Specify here if a greater load is required.
**********************************************************************************************************

Built-in gutter systems where drainage passes through an interior space or is concealed in the exterior cavity wall is prohibited.

Refer to     Unified Facilities Criteria (UFC) 3-110-03, Roofing, UFC 3-101-01, Architecture, and UFC 1-200-02, High Performance Sustainable Building Requirementsfor additional roofing requirements.

[The project is an addition to an existing building, and the roof system of the addition must match the roof of the existing building, which is ______.]

B3010 ROOF COVERINGS

B301001 STEEP SLOPE ROOFING SYSTEMS

Steep slope roofing systems are preferred over low slope roofing systems, where practical.  Steep slope roofing systems that are acceptable include galvanized metal as shown on the definitive drawings.

Any redesign of the roof system must be designed and attached to resist wind uplift pressures calculated in accordance with     American Society of Civil Engineers (ASCE) 7.  Uplift resistance shall be validated by applicable Factory Mutual (FM), Underwriters Laboratories (UL) or     American Society for Testing and Materials (ASTM) uplift resistance test procedures. [Steel panels must be zinc-coated steel conforming to ASTM A 653/A 653M; aluminum-zinc alloy coated steel conforming to ASTM A 792/A 792M, AZ [55] [50] coating; or aluminum-coated steel.]

[Provide [galvanized] [shop painted] sub-purlins for the Structural Metal Roof System.]

********************************************************************************************************** 
NOTE: For Structural Standing Seam Metal Roofing Systems, specify here the 5-year or the 5-year plus 20-year warranties.
**********************************************************************************************************

********************************************************************************************************** 
NOTE:  Few manufacturers regularly produce prefinished panels meeting these low gloss requirements and such sheets are available only in limited colors.  Standard 70 percent     (polyvinylidene fluoride) PVF2 finish, for example, has a medium gloss.  Low gloss paint formulations result in reduced weathering properties.  The project program must dentify individual facilities requiring low gloss finish.
For roof of structures at airfields where glare would be objectionable and may be an operational hazard, the specular gloss value should be limited to 10 or less at an angle of 85 degrees.
**********************************************************************************************************

B301004 FLASHINGS AND TRIM

Flashing and sheet metal work includes scuppers, splash pans, and sheet metal roofing.  Flashings shall be [copper, sheet and strip - ASTM B 370, cold-rolled temper] [Lead-Coated Copper Sheet - ASTM B 101] [Lead Sheet - Minimum weight .19 kPa (4 pounds per square foot)] [Steel Sheet, Zinc-Coated (Galvanized) - ASTM A 653/ A 653M, minimum of 0.70 mm (24 gauge) and a minimum zinc coat weighting of 275 g/sm (90 ounces per square feet).] [Galvanized steel items shall have a baked-on, factory applied finish of polyvinylidene fluoride or an equivalent fluorocarbon coating] [Steel Sheet, Aluminum Zinc -coated - ASTM A792/A792M, minimum of 0.70 mm (24 gauge)] [Stainless Steel - ASTM A 167, Type 302 or 304, minimum of 0.64 mm (24 gauge] [Aluminum Alloy Sheet and Plate - ASTM B 209] [Pre-Finished Aluminum. Finish shall be baked-on factory applied color coating of polyvinylidene fluoride (PVF2) or other equivalent fluorocarbon coating with a minimum thickness of 0.8 to 1.3 mils].

--End of Section--