*************************************************************************** 
NAVFAC                                                 PTS-A20 (December 2018)
                                             ------------------------------
Preparing Activity: NAVFAC                  SUPERSEDING PTS-A20 (February 2018)

PERFORMANCE TECHNICAL SPECIFICATION

***************************************************************************

SECTION A20

BASEMENT CONSTRUCTION
12/18

*************************************************************************** 
NOTE:  This section is intended to be used as a guide and contains requirements that are common to many different types of facilities. In addition, there may be special requirements for a particular project that are not addressed at all.  The RFP preparer will need to incorporate additional information to address these special requirements in this PTS and corresponding Part 3 ESR.  If the RFP Preparer chooses to delete building elements that are not required for the project, do not change the remaining Uniformat paragraph designations (example A102001).  Uniformat designations are unique to the products they are assigned to.  However, the subparagraphs numerical extension (example – 1.2 or a,b,c of the Uniformat designations may change if subparagraphs are deleted).

This guide specification is formatted utilizing Uniformat II, an industry recognized standard, ASTM E 1557.  When the RFP preparer chooses to add a paragraph that does not apply to an existing building element already included in the specification, refer to the Uniformat/WBS located on the NAVFAC Design-Build Website for a listing of Uniformat II designations and definitions.

NOTE:  The RFP preparer may view or hide the criteria notes in this PTS section by modifying the WORD preferences for "Hidden text".  To view the criteria notes, choose "File" then "Option".  Click "Display" then check the "Hidden text" box under "Always show these formatting marks on the screen".  In the same section, check the box for "Print hidden text" under "Printing options" to print the criteria notes.
 ***************************************************************************

*************************************************************************** 
The Table of Contents is intended for navigation purposes only for the RFP writer and should not show up in the printed document.

TABLE OF CONTENTS

A20     GENERAL
A20  1.1  DESIGN GUIDANCE
A20  1.2  GENERAL REQUIREMENTS
A20  1.3  PERFORMANCE VERIFICATION AND ACCEPTANCE TESTING
A20  1.4  DESIGN SUBMITTALS
A20  1.5  CONSTRUCTION SUBMITTALS
A2010     BASEMENT EXCAVATION
A201001     EXCAVATION FOR BASEMENTS
A201002     STRUCTURE BACKFILL AND COMPACTION
A201003     SHORING
A2020     BASEMENT WALLS
A202001     BASEMENT WALL CONSTRUCTION
A202002     MOISTURE PROTECTION
A202002  1.1  BUILT-UP BITUMINOUS WATERPROOFING
A202002  1.2  ELASTOMERIC SHEET WATERPROOFING
A202003     BASEMENT WALL INSULATION
A202003  1.1  BLOCK OR BOARD INSULATION
A202003  1.2  BLANKET INSULATION
A202004     INTERIOR SKIN
***************************************************************************

A20 GENERAL

RFP Part 3 including the Engineering System Requirements (ESR) provide project specific requirements.  The RFP Part 4, Performance Technical Sections (PTS) provide generalized technical requirements that apply to multiple facility types and include more requirements than are applicable to any one project. Therefore, only the RFP Part 4 requirements that apply to the project and further define the RFP Part 3 project specific requirements are required.

A20 1.1 DESIGN GUIDANCE

Provide the design and installation in accordance with the following references.  This Performance Technical Specification (PTS) adds clarification to the fundamental requirements contained in the following Government Standards.  The general requirements of this PTS section are located in PTS Section Z10, General Performance Technical Specification.

A20 1.1.1 Government Standards

UNIFIED FACILITIES CRITERIA (UFC)

| UFC 1-200-01 | DoD Building Code (General Building Requirements)(A reference in this PTS section to UFC 1-200-01 requires compliance with the Tri-Service Core UFCs that are listed therein, which includes the following significant UFC(s):UFC 3-101-01, ArchitectureUFC 3-220-01, Geotechnical EngineeringUFC 3-301-01, Structural Engineering) |
| --- | --- |

UNIFIED FACILITIES GUIDE SPECIFICATIONS (UFGS)

| UFGS Section 31 23 00.00 20 | Excavation and Fill |
| --- | --- |

A20 1.2 GENERAL REQUIREMENTS

A20 1.2.1 Required Specifications

The Designer of Record shall utilize the following UFGS Specifications for the project specification.

Section 31 23 00.00 20, Excavation and Fill

*************************************************************************** 
NOTE:  Modify the paragraph below to correspond with the subsurface soils information that is being provided.  If subsurface soils information is to be provided, assure that the information is included in Part 6 of the RFP.
***************************************************************************

A20 1.3 PERFORMANCE VERIFICATION AND ACCEPTANCE TESTING

Provide verification of satisfactory construction and system performance of the basement via Performance Verification Testing, and by field inspection, as detailed in this section of the RFP.

A20 1.3.1 Earthwork

Perform quality assurance for earthwork in accordance with     International Building Code (IBC) Chapter 17 and UFGS Section 31 23 00.00 20.  If a registered Professional Engineer is required to provide inspection of excavations and soil/groundwater conditions throughout construction, the Engineer must perform pre-construction and periodic site visits throughout construction to assess site conditions.  The Engineer, with the concurrence of the Contractor and the Contracting Officer,  must update the excavation, sheeting, shoring, and dewatering plans as construction progresses to reflect actual site conditions and must submit the updated plan and a written report (with professional stamp) at least monthly informing the Contractor and the Contracting Officer of the status of the plan and an accounting of Contractor adherence to the plan; specifically addressing any present or potential problems.  The Engineer must be available to meet with the Contracting Officer at any time throughout the contract duration.  Provide the services of the Engineering at no additional cost to the Government.

*************************************************************************** 
NOTE: NAVFAC has made every effort to use commercial standards in the PTS Sections. If project requirements dictate the use of a UFGS Section as a standard, add a paragraph here listing the required UFGS Section. State in the paragraph that the DOR must edit this UFGS Section in accordance with PTS Z10 and submit it as a part of the design submittal.
***************************************************************************

A202001 BASEMENT WALL CONSTRUCTION

Provide basement walls as required in accordance with the requirements of this section and other portions of this RFP.

A202002 MOISTURE PROTECTION

A202002 1.1 BUILT-UP BITUMINOUS WATERPROOFING

A202002 1.1.1 Environmental Conditions

Apply the primers and waterproofing specified herein when the ambient temperature is above 40 degrees F.

A202002 1.1.2 Liquid Asphalt

Deliver bulk liquid asphalt in fully insulated, heated transport tanker vehicles with circulating pump devices.  Maintain the temperature of the liquid asphalt between 400 and 450 degrees F during storage, provided the transport and storage time does not exceed 12 hours.  If the transport and storage time exceeds 12 hours, lower the temperature to between 300 and 325 degrees F at the time the 12 hours are exceeded.  Use liquid asphalt within 36 hours after loading in the transport tanker.

A202002 1.1.3 Materials

a.	Bitumen - Asphalt;     American Society for Testing and Materials (ASTM) D 449, Type I.

b.	Bituminous Plastic Cement - ASTM D 4586, Type I for asphalt.

c.	Membrane Fabric

 The following requirements apply:

 Felt or Fabric      Saturant or
Material            Impregnant        Specification

 Glass (felt) mat     Asphalt       ASTM D 2178, Type III
Reinforcing glass    Asphalt       ASTM D 1668, Type I
fabric

d.	Nails - Galvanized roofing nails.

e.	Primer - ASTM D 41 for asphalt.

f.	Protection Board - ASTM D 517, plain, asphalt plank; ASTM C 208, construction grade building board, 1/2 inch thick, asphalt saturated or coated; ASTM C 726, 7/16 inch thick, covered on one side with waterproof paper or asphalt-saturated felt.

A202002 1.2 ELASTOMERIC SHEET WATERPROOFING

A202002 1.2.1 Environmental Conditions

Do not apply waterproofing during inclement weather or when there is ice, frost, surface moisture, or visible dampness on the surface to receive waterproofing and when ambient and surface temperatures are 40 degrees F or below.  The restriction on the application of waterproofing materials when ambient and surface temperatures are below 40 degrees F will be waived if the Contractor devises a means, approved by the Contracting Officer, of maintaining the surface and ambient temperatures above 40 degrees F.

A202002 1.2.2 Butyl Rubber Sheeting

Not less than 60 mils minimum thickness.

A202002 1.2.2.1 Butyl Rubber Sheeting Performance Requirements

a.	Thickness Tolerance, ASTM D 412:  Plus or minus 10 percent;

b.	Specific Gravity, ASTM D 297:  1.20, plus or minus 0.05;

c.	Tensile Strength, ASTM D 412:  1200 psi minimum;

d.	Tensile Stress at 300 percent elongation, ASTM D 412:  600 psi minimum;

e.	Elongation, ASTM D 412:  300 percent minimum;

f.	Tear Resistance, Die C, ASTM D 624:  125 pound force per inch (lbf/inch) minimum;

g.	Shore A Hardness, ASTM D 2240:  Five-second interval before reading; 60 plus or minus 10;

h.	Ozone Resistance, ASTM D 1149:  No cracks, 7 days - 50 pphm -  100 degrees F, 20 percent elongation;

i.	Heating Aging-Accelerated, ASTM D 573:  Tensile retention, 60 percent of minimum original elongation retention; 60 percent of minimum original requirement;  7 days, 240 degrees F.

j.	Butyl Identification, ASTM D 471, Tricresyl Phosphate Immersion:  Maximum volume swell 10 percent, 70 hrs, 212 degrees F;

k.	Low Temperature Flexibility, ASTM D 746:  No failure at  -40 degrees F;

l.	Water Absorption, ASTM D 471:  +1 percent maximum.  7 days, 158 degrees F;

m.	Exposure to Fungi and Bacteria in Soil, Minimum 16 Weeks: Unaffected; and

n.	Water Vapor Transmission, 80 Degrees F Permeance, ASTM E 96, Procedure B or BW: 0.15 perms maximum.

A202002 1.2.2.2 Adhesive, Cement, and Tape for Use with Butyl Rubber

Provide as recommended by the butyl rubber waterproofing membrane manufacturer.

A202002 1.2.3 Composite, Self-Adhering Membrane Sheeting

Cold applied composite sheet consisting of rubberized asphalt and cross laminated, high-density polyethylene film. Not less than 60 mils minimum thickness is required.

A202002 1.2.3.1 Composite, Self-Adhering Sheeting Performance Requirements

a.	Tensile Strength, ASTM D 412, Die C:  250 psi minimum;

b.	Ultimate Elongation, ASTM D 412, Die C:  200 percent minimum;

c.	Water Vapor Transmission, ASTM E 96 80 Degrees F Permeance, Procedure B: 0.1 perm maximum;

d.	Pliability Degrees F, ASTM D 146: (180 Degrees Bend Over One Inch Mandrel):  No cracks at minus -25 degrees F;

e.	Cycling Over Crack at Minus 15 Degrees F: Membrane is applied and rolled across two primed concrete blocks with no separation between blocks.  Crack opened and closed from zero to 1/4 inch.  No effect at 100 cycles;

f.	Puncture Resistance, ASTM E 154:  40 lb. minimum;

g.	Lap Adhesion at Minimum Application Temperature, ASTM D1876 Modified, 5 lbs/in.(880 N/m);

h.	Peel Strength, ASTM D 903: Modified, 9 lbs/in;

i.	Resistance to Hydrostatic Head, ASTM D 5385: 231 ft of water

j.	Water Absorption, ASTM D 570; 0.1% maximum.

A202002 1.2.3.2 Primer

Asphalt composition, ASTM D 41, or synthetic polymer in solvent as recommended by the membrane manufacturer.

A202002 1.2.3.3 Mastic

Polymer modified asphalt in suitable solvent of trowel-grade consistency and as recommended by the membrane manufacturer.

A202002 1.2.4 Protection Board

Three-dimensional, high impact resistant polymeric grid with woven monofilament drainage fabric bonded to the grid.

-- End of Section --